## Slide 1: ECE 424 Embedded Systems Design
Embedded Linux Overview
Chapter 8
Ning Weng

## Slide 2: What’s so special about Linux?
Multiple choices vs. sole source
Source code freely available
Robust and reliable
Modular, configurable, scalable
Superb support for networking and Internet
No runtime licenses
Large pool of skilled developers

## Slide 3: What is a good Embedded OS?
Modular
Scalable
Configurable
Small footprint
CPU support
Device drivers
Etc.

## Slide 4: Commercial Embedded Linux
AMIRIX Embedded Linux
  derived from Debian
Coollogic Coollinux
  combines Linux and Java for Internet apps
Coventive Xlinux
  kernel can be as small as 143KB
Esfia RedBlue Linux
  400K, designed for wireless apps
And many others

## Slide 5: Open Source Embedded Linux
Embedded Debian Project
  convert Debian to an embedded OS
ETLinux
  for PC104 SBC’s
uCLinux
  for microprocessors that don’t have MM
uLinux (muLinux)
  fits on a single floppy

## Slide 6: What’s so special about Linux?

## Slide 7: Tool Chains
Necessary to build OS and apps
Most common are the GNU tools
Normally the target and host machine compile and build with the same environment
  Host: the machine on which you develop your applications
  Target: the machine for which you develop your applications
  Native development (same) or cross development (different)

## Slide 8: Tool Chains

## Slide 9: Getting Tool

## Slide 10: Anatomy of Embedded Linux
Kernel
Device Drivers
Root File System

## Slide 11: Packages Dependencies
FIGURE 8.1 Package Dependencies for the Bash shell – Bash Package.

## Slide 12: The Kernel
Kernel steps:
Download the source tree
Run the tool to create the kernel .config
Build the kernel
End kernel steps
Root file system
Busybox
C library
Boot sequence

## Slide 13: The Kernel Steps

## Slide 14: Sample Directories in Kernel Tree

## Slide 15: The Kernel (kernel step 2)
Three options are generated in the .config file:
CONFIG_FEATURE_XX=y
#CONFIG_FEATURE_XX not set
CONFIG_FEATURE_XX=m
EX: Xscale Intel IXP435 BSP configuration change
machine_is_ixp425()
CONFIG_MACH_IXP425
MACH_TYPE_IXP425

## Slide 16: The Kernel (kernel step 3)
Why Compressed kernel image?

## Slide 17: Root File System
the filesystem that is contained on the same partition on which the root directory is located,
the filesystem on which all the other filesystems are mounted (i.e., logically attached to the system) as the system is booted up (i.e., started up).
Filesystem Hierarchy Standard (FHS)
  /bin
  /dev
  /etc
  /lib
  /lib/modules
  /proc
  /root
  /sbin
  /sys
  /tmp
  /usr
  /var

## Slide 18: Busybox
BusyBox combines tiny versions of many common UNIX utilities into a single small executable.
It provides replacements for most of the utilities you usually find in GNU fileutils, shellutils, etc.
The utilities in BusyBox generally have fewer options than their full-featured GNU cousins; however, the options that are included provide the expected functionality and behave very much like their GNU counterparts.
BusyBox provides a fairly complete environment for any small or embedded system.

## Slide 19: Static or Dynamic Link

## Slide 20: The Kernel (C Library)
Libc: standard
GLIBC: GNU C Library
EGLIBC: Embedded GLIBC
uCLIBC: much smaller than GLIBC
Bionic C: used by Android

## Slide 21: The Kernel (Boot Sequence)
BIOS or early firmware
  The first code execute by cpu after out o reset
  Initializing memory and boot devices
Boot loader
  Elilo/grub2
  Find the kernel and copy into memory and handoff to kernel
Kernel image
  bzImage
  Mass storage, along with root file system and application
  Dedicated flash area
Root file system
  Applications, libraries and scripts
  Example: NFS: a directory on the host as root file system of target

## Slide 22: Debugging
Debugging Applications (GDB, Kdevelop, Eclipse)
Kernel debugging
QEMU Kernel Debugging

## Slide 23: Driver Development
Functions of device driver:
Abstracts the hardware
Manages privilege
Enables multiplexed access
Martials Data from an application’s process to kernel space
Provides security

## Slide 24: Character Driver Model

## Slide 25: Driver Demo

## Slide 26: Device Driver
General PCI device drivers Steps
Enable device
Request memory-mapped I/O Regions
Set the DMA mask size
Allocate and Initialize shared control data
Access device configuration space (if needed)
Manage the allocation of MSI/x interrupt vectors
Initialize the non-PCI capabilities
Register with other kernel sub systems
Enable the device for processing
Note: In addition to the above, networking drivers must register functions to allow TCP/IP networking stack to interact with the adaptor to transmit and receive packets.

## Slide 27: Driver Development (interrupt handling & deferred work)
Interrupts:
Legacy Interrupts (INTA/ INTB/ INTC/ INTD)
Message Signal Interrupts (MSI)
Message Signal Interrupts eXtension (MSIx)
Methods to defer work from interrupt handler:
SoftIRQs
Tasklets =>
Work Queues

## Slide 29: Memory Management

## Slide 30: Synchronization/Locking
Primitives for synchronization and locking mechanisms to race free code
Atomic Operation: runs without being interrupted
  Use processor atomic instructions such as TSL (test set and lock), and Locked CMPXCHG (locked compare and exchange)

## Slide 31: Synchronization/Locking
2. Spinlock: lock with busy wait

## Slide 32: Synchronization/Locking
3. Semaphore: lock with blocking wait (sleep)

## Slide 33: Conclusion
Tool Chains
The Kernel
Debugging
Driver Development
Memory Management
Synchronization/Locking

## Slide 34: Announcement
Next class: Power Optimization
Exam ii: 10/31

## Slide 35: Embedded Linux Programming
Cross-compiling (By ARM’s example)
Source
Code
Files
(a.c, b.c)
ARM
Object
Files
(a.o, b.o)
Cross-
Compile
Link
ARM
Executable
File
(hello)
ARM
Library
Files
(libm.a)
Linux# arm-elf-gcc a.c –o a.o
Linux# arm-elf-gcc b.c –o b.o
Linux# arm-elf-ld a.o b.o –lm –o hello

## Slide 36: Embedded Linux Programming
Setup cross compile environment
  For Linux
    Download and install the Linux toolchain for your target board such as arm-elf- tools.
    Example: Toolchain for ARM
      First, download from uClinux.org or somewhere.

## Slide 37: Embedded Linux Programming
      Second, install it to the proper directory. (eg. /usr/local/)
You have the toolchain
installed on your system.
Extract the tools from
downloaded package.

## Slide 38: Embedded Linux Programming
  For Windows
    Ordinarily, you have to install CYGWIN to provide a Linux-like environment on Windows.

## Slide 39: Embedded Linux Programming
    Download and install the toolchain as described before.
    Note that the toolchain must be compiled for CYGWIN.
Figure:
Cygwin provides
a Linux-like
Environment.

## Slide 40: Embedded Linux Programming
Linux system programming
  Low-level File I/O
    open(), read(), write(), close(), creat(), fnctl() …
#include <unistd.h>
#include <stdlib.h>
…
int main()
{
…
/* Open /tmp/in.txt and /tmp/out.txt*/
fd1 = open(“/tmp/in.txt”, O_RDONLY | O_CREAT);
fd2 = open(“/tmp/out.txt”, O_WRONLY | O_CREAT);
if ((read(fd1, buffer, sizeof(buffer)) != sizeof(buffer))
…
if ((write(fd2, buffer, sizeof(s)) != sizeof(s))
…
close(fd1); close(fd2);
}

## Slide 41: Embedded Linux Programming
  Process
    execl(), fork(), exit(), system(), wait(), getpid() …
#include <unistd.h>
…
int main()
{
pid_t new_pid;
new_pid = fork();
switch (new_pid) {
case -1 :
printf ("fork failed\n"); exit(1); break;
case 0 :
printf ("This is the child process.pid = %d\n“, getpid()); break;
default:
printf ("This is the parent process, pid = %d.\n“, getpid());
}
return 0;
}

## Slide 42: Embedded Linux Programming
  Thread
    pthread_create(), pthread_join(), pthread_cancel() …
#include <pthread.h>
…
/* Prints x’s to stderr. The parameter is unused. Does not return. */
void* print_xs (void* unused)
{
while (1)
fputc (‘x’, stderr);
}
int main ()
{
pthread_t thread_id;
/* Create a new thread to run the print_xs function. */
pthread_create (&thread_id, NULL, &print_xs, NULL);
/* Print o’s continuously to stderr. */
while (1)
fputc (‘o’, stderr);
return 0;
}

## Slide 43: Embedded Linux Programming
  IPC
    mmap(), munmap(), msgctl(), msgget(), msgsnd() …
…
int main (int argc, char* const argv[])
{
…
void* file_mem;
…
/* Prepare a file large enough to hold an unsigned integer. */
fd = open (argv[1], O_RDWR | O_CREAT, S_IRUSR | S_IWUSR);
lseek (fd, LENGTH+1, SEEK_SET);
…
/* Create the memory mapping. */
file_mem = mmap (0, LENGTH, PROT_WRITE, MAP_SHARED, fd, 0);
…
/* Write a random integer to memory-mapped area. */
sprintf((char*) file_mem, “%d\n”, random_range (-100, 100));
/* Release the memory (unnecessary because the program exits). */
munmap (file_mem, LENGTH);
return 0;
}

## Slide 44: Embedded Linux Programming
  Signal
    signal(), alarm(), kill(), pause(), sleep() …
#include <signal.h>
…
void ouch (int sig)
{
printf ("OUCH! I got signal %d\n", sig);
signal (SIGINT, SIG_DFL);
}
main()
{
signal (SIGINT, ouch); /* Install handler for SIGINT */
while(1) /* Infinite loop until Ctrl + C is pressed */
{
printf ("Hello World!\n");
sleep(1);
}
}

## Slide 45: Embedded Linux Programming
  Socket
    socket(), accept(), connect(), recv(), send() …
#include <sys/types.h>
…
main()
{
…
/* Create a socket … */
sd = socket(AF_INET,SOCK_STREAM,0);
…
/* Accept for connections and return a new socket description id
for handling the connection */
newsd = accept(sd, (struct sockaddr *) &ser_cli, &addrlen);
if(newsd < 0)
{
printf("cannot accept \n");
exit(1);
}
…
}

## Slide 46: Embedded Linux Programming
uClinux for Linux programmers [11]
  Important issue  Do not support VM.
  Each process must be located at a place in memory where it can be run.
  The area of process memory must be contiguous.
  Cannot increase the size of its available memory at runtime.
  ELF executable file format is unsupported  FLAT format instead.

## Slide 47: Embedded Linux Programming
  The implementation of mmap() within the kernel is also quite different.
  The only filesystem that currently guarantees that files are stored contiguously  romfs.
  Only read-only mappings can be shared  To avoid the allocation of memory.
  Copy-on-write feature is unsupported  Use vfork() instead of fork(). (Discuss later)
  The stack must be allocated at compile time  Must be aware of the stack requirements.

## Slide 48: Embedded Linux Programming
  fork() vs. vfork()
.
.
.
fork()
.
.
.
Data
.
.
write()
.
.
Dynamic
allocated
Copy-on-write
Non-blocking
.
.
.
fork()
.
.
.
Data
.
.
write()
.
exit()
Use parent’s stack and data
may corrupt the data or the stack in the parent.
Suspended
Continue
executing
fork()
vfork()
Parent
Parent
Child
Child

## Slide 49: Embedded Linux Programming
Example: A DHCP Client: udhcp (script.c)
void run_script(struct dhcpMessage *packet, const char *name)
{
…
envp = fill_envp(packet);
/* call script */
pid = vfork();
if (pid) { /* Parent */
waitpid(pid, NULL, 0);
…
} else if (pid == 0) { /* Child */
/* exec script */
execle(client_config.script, client_config.script, name, NULL, envp);
exit(1);
}
}

## Slide 50: Embedded Linux Programming
Linux device driver fundamentals [12]
Figure:
The split view
of the kernel.

## Slide 51: Embedded Linux Programming
The role of device driver
  To allow interaction with hardware devices.
  Providing mechanism, not policy.
    What capabilities are to be provided?  mechanism
    How those capabilities can be used?  policy
Writing a Linux device driver
  Pre-requisites
    C programming
    Microprocessor programming
  Important concepts
    User space vs. kernel space

## Slide 52: Embedded Linux Programming
Execution paths: From user to kernel

## Slide 53: Embedded Linux Programming
Classes of devices
  Characters devices
    Can be accessed as a stream of bytes.
    Such a driver usually implements at least the open, close, read, and write system calls.
    Example: RTC driver.
  Block devices
    A device (e.g., a disk) that can host a filesystem.
    Example: Ramdisk driver.
  Network interfaces
    In charge of sending and receiving data packets, driven by the network subsystem of the kernel.
    Example: Network card driver.

## Slide 54: Embedded Linux Programming
Kernel Module: Life and Death
Figure:
Linking a module
to the kernel. [12]

## Slide 55: Embedded Linux Programming
The first kernel module “Hello, world”
#include <linux/init.h>
#include <linux/module.h>
MODULE_LICENSE(“Dual BSD/GPL”);
static int hello_init(void)
{
printk(KERN_ALERT “Hello, world\n”);
return 0;
}
static void hello_exit(void)
{
printk(KERN_ALERT “Goodbye, cruel world\n”);
}
module_init(hello_init);
module_exit(hello_exit);

## Slide 56: Embedded Linux Programming
Some other types of kernel modules
  USB Module
  Serial Module
  SCSI Module
  PCI Module
  I2C Module
  Misc Module
  …
Topics you also need to be concerned about
  Memory allocating
  Interrupt handling
  Concurrency and race condition
  I/O accessing
  Time, delays and deferred work